# Upgrade to ACME screws
You may start upgrading you Piper 3d printer by installing ACME screws instead of 5/16 rods.
# Upgrade to heated bed.
To upgrade to heated bed you may have several options. Those options depend on the size of the bed.

Bed size	Heating element wattage	Heat bed voltage	Example of parts	Notes
200mm x 200mm	200+ W	12 V is sufficient	Heated bed	you need a separate SSR as Ramps 1.4 does not provide enough current
200mm x 300mm	300+ W	You may need a separate PSU or move to 24V PSU		may require changes to Ramps 1.4 board
300mm x 300mm	450+ W	You need 110V(220V) heat panel, SSR DC to AC 25A and be very careful as moving pate will have wires with high voltage.		This is not recommended configuration since wires with high voltage will be constantly bended by moving bed, failure in wires may cause electrical shock.