# This file serves as documentation for config parameters of corexy
# style printers. One may copy and edit this file to configure a new
# corexy printer. Only parameters unique to corexy printers are
# described here - see the "example.cfg" file for description of
# common config parameters.

# DO NOT COPY THIS FILE WITHOUT CAREFULLY READING AND UPDATING IT
# FIRST. Incorrectly configured parameters may cause damage.

# The main micro-controller is used as the timing source for all the
# micro-controllers on the printer. Typically, both the X and Y axes
# are connected to the main micro-controller.
[mcu]

serial: /dev/ttyACM0
#serial: /dev/serial/by-path/pci-0000:00:14.0-usb-0:2:1.0-port0
#serial: /dev/serial/by-path/pci-0000:00:14.0-usb-0:1:1.0-port0
#pin_map: arduino
#baud: 250000

# Support manually moving stepper motors for diagnostic purposes.
# Note, using this feature may place the printer in an invalid state -
# see docs/G-Codes.md for important details.
[force_move]
enable_force_move: true

# Set to true to enable FORCE_MOVE and SET_KINEMATIC_POSITION
# extended G-Code commands. The default is false.

# The "zboard" micro-controller will be used to control the Z axis.
[mcu z]
#serial: /dev/serial/by-path/pci-0000:00:14.0-usb-0:1:1.0-port0
#serial: /dev/serial/by-path/pci-0000:00:14.0-usb-0:2:1.0-port0
serial: /dev/ttyUSB0
pin_map: arduino
baud: 250000

#test INIT_TMC STEPPER=stepper_y DUMP_TMC STEPPER=stepper_y
[board_pins]
aliases:
    # EXP1 header
    EXP1_1=P1.30, EXP1_3=P1.18, EXP1_5=P1.20, EXP1_7=P1.22, EXP1_9=<GND>,
    EXP1_2=P0.28, EXP1_4=P1.19, EXP1_6=P1.21, EXP1_8=P1.23, EXP1_10=<5V>,
    # EXP2 header
    EXP2_1=P0.17, EXP2_3=P3.26, EXP2_5=P3.25, EXP2_7=P1.31, EXP2_9=<GND>,
    EXP2_2=P0.15, EXP2_4=P0.16, EXP2_6=P0.18, EXP2_8=<RST>, EXP2_10=<NC>
    # Pins EXP2_1, EXP2_6, EXP2_2 are also MISO, MOSI, SCK of bus "ssp0"

# stepper controlling the X+Y movement.
[stepper_y]
step_pin: P0.19
dir_pin: !P0.20
enable_pin: !P2.8
#step_distance: 0.2
step_distance: 0.0125 #SHould be 0.0125 for 1/16 micro-steppting
##step_distance: 0.00625
endstop_pin: tmc2130_stepper_y:virtual_endstop
homing_retract_dist: 0
position_endstop: 0
position_min: 0
position_max: 500
homing_speed: 60

[tmc2130 stepper_y]
cs_pin: P1.15
spi_software_miso_pin: P0.5
spi_software_mosi_pin: P4.28
spi_software_sclk_pin: P0.4
diag1_pin: !P1.27
microsteps: 16
interpolate: True
run_current: .80 #Try 0.75 to 0.85 by 0.05 increments
hold_current: .5 #Set to 0.75
stealthchop_threshold: 0
driver_PWM_GRAD: 10
driver_SGT: 4

# The stepper_y section is used to describe the Y axis as well as the
# stepper controlling the X-Y movement.
[stepper_x]
step_pin: P2.2
dir_pin: P2.6
enable_pin: !P2.1
step_distance: 0.0125 #SHould be 0.0125 for 1/16 micro-steppting
#step_distance: 0.00625
endstop_pin: tmc2130_stepper_x:virtual_endstop
homing_retract_dist: 0
position_endstop: 0
position_max: 500
position_min: 0
homing_speed: 60

[tmc2130 stepper_x]
cs_pin: P1.17
spi_software_miso_pin: P0.5
spi_software_mosi_pin: P4.28
spi_software_sclk_pin: P0.4
diag1_pin: !P1.29
microsteps: 16
interpolate: True
run_current: .80 #Try 0.75 to 0.85 by 0.05 increments
hold_current: .5 #Set to 0.75
#run_current: 1.2 #Try 0.75 to 0.85 by 0.05 increments
#hold_current: .5 #Set to 0.75
#sense_resistor: 0.110
stealthchop_threshold: 0
driver_PWM_GRAD: 10
driver_SGT: 11

[stepper_z]
# Z stepper pins on MCU Z
step_pin: z:ar60
dir_pin: z:ar61
enable_pin: !z:ar56
step_distance: 0.000625
# probe:z_virtual_endstop is a virtual pin definition only available if
# a probe section is defined
endstop_pin: probe:z_virtual_endstop
# mechanical switch on mcu Z X min endstop pin
##endstop_pin: ^!z:ar19
#position_endstop: -0.376
position_min: -5
position_max: 500
homing_speed: 5

[stepper_z1]
# X stepper pins on MCU Z
step_pin: z:ar54
dir_pin: z:ar55
enable_pin: !z:ar38
step_distance: 0.000625

[stepper_z2]
# E0 stepper pins on MCU Z
step_pin: z:ar26
dir_pin: z:ar28
enable_pin: !z:ar24
step_distance: 0.000625

[stepper_z3]
# E0 stepper pins on MCU Z
step_pin: z:ar46
dir_pin: z:ar48
enable_pin: !z:ar62
step_distance: 0.000625

#[servo toolS]
#pin: z:ar42
#maximum_servo_angle: 300
### The maximum angle (in degrees) that this servo can be set to. The
### default is 180 degrees.
##minimum_pulse_width: 0.0005
### The minimum pulse width time (in seconds). This should correspond
### with an angle of 0 degrees. The default is 0.001 seconds.
#maximum_pulse_width: 0.003
#initial_angle: 120

[probe]
pin: ^!z:ar18
z_offset: 1.82
y_offset: 5
x_offset: 0
speed: 5.0

#[homing_override]
#set_position_z: 0
#axes: z
#gcode:
# G90 ; Uncomment these 2 lines to blindly lift the Z 2mm at start
# G1 Z10 F600
# G28 X0 Y0
# G1 X250 Y250 F3600
# G28 Z0

[homing_override]
set_position_z: 0
axes: z
gcode:
    G90 ; Uncomment these 2 lines to blindly lift the Z 2mm at start
    G1 Z8 F600
    G28 X0 Y0
    G1 X250 Y250 F3600
    G28 Z0
    G1 Z10 F600

#[temperature_sensor Host_temp]
#sensor_type: temperature_host
#sensor_path: /sys/bus/platform/drivers/coretemp/coretemp.0/hwmon/hwmon1/temp2_input
#gcode_id:S

[adc_temperature my_sensor]
#temperature1: 28
#voltage1: 0.8

temperature1: 26.5
voltage1: 0.822

temperature2: 50.3
voltage2: 0.914

temperature3: 75.5
voltage3: 1.012

temperature4:100.6
voltage4:1.106

temperature5:150.4
voltage5:1.289

temperature6:200.1
voltage6:1.464

temperature7:225.1
voltage7:1.547

temperature8:250.8
voltage8:1.623

#temperature1: 221
#resistance1:
#temperature2:
#resistance2:

[thermistor winsinn_ht-ntc100k]
temperature1: 25
resistance1: 100000
temperature2: 80
resistance2: 8300
temperature3: 220
resistance3: 127

[extruder]
step_pin: P2.13
dir_pin: !P0.11
enable_pin: !P2.12
#step_distance: 0.010476
step_distance: 0.0024145313708312
nozzle_diameter: 0.400
filament_diameter: 1.750
max_extrude_cross_section: 20.0
max_extrude_only_distance: 950.0
max_extrude_only_accel: 10000
#pressure_advance: 0.0
#pressure_advance_lookahead_time: 0.010
#pressure_advance: 0.45
#pressure_advance_lookahead_time: 0.02
heater_pin: P2.7

######sensor_type: winsinn_ht-ntc100k
######sensor_pin: P0.24
######pullup_resistor: 4700

######sensor_type: ATC Semitec 104GT-2
sensor_type: NTC 100K beta 3950
sensor_pin: P0.24

#sensor_type: PT100 INA826
#adc_voltage: 3.2
#sensor_pin: P0.2
#voltage_offset: 0.48

#PT100
#sensor_type: my_sensor
#adc_voltage: 3.275
#sensor_pin: P0.2

#sensor_type: NTC 100K beta 3950
#sensor_type: EPCOS 100K B57560G104F
#sensor_type: NTC 100K MGB18-104F39050L32
#sensor_type: Honeywell 100K 135-104LAG-J01
#control: watermark
min_temp: 0
max_temp: 500

#[extruder1]
#step_pin: z:ar36
#dir_pin: !z:ar34
#enable_pin: !z:ar30
#step_distance: 0.0024145313708312
#nozzle_diameter: 0.400
#filament_diameter: 1.750
#max_extrude_cross_section: 20.0
#max_extrude_only_distance: 950.0
#max_extrude_only_accel: 10000
#pressure_advance: 0.0
#pressure_advance_lookahead_time: 0.010
#pressure_advance: 0.45
#pressure_advance_lookahead_time: 0.02
#heater_pin: z:ar10
#sensor_pin: z:analog13
##sensor_type: ATC Semitec 104GT-2
#sensor_type: NTC 100K beta 3950
#sensor_type: EPCOS 100K B57560G104F
#sensor_type: NTC 100K MGB18-104F39050L32
#sensor_type: Honeywell 100K 135-104LAG-J01
#control: watermark
#min_temp: 0
#max_temp: 300
#pid_Kp: 22.2
#pid_Ki: 1.08
#pid_Kd: 114

[heater_fan my_nozzle_fan]
pin: z:ar9
heater: extruder
heater_temp: 50.0
fan_speed: 1.0

[heater_bed]
heater_pin: P2.5
sensor_type: NTC 100K beta 3950
sensor_pin: P0.23
#control: watermark
min_temp: 0
max_temp: 150

[verify_heater heater_bed]
# adjust for personal bed setup, this prevents stock heated bed from issuing
# false positive heating errors due to slow temperature increase
check_gain_time: 900

[verify_heater extruder]
check_gain_time: 120
heating_gain: 1
max_error: 260

#[verify_heater extruder1]
#check_gain_time: 60
[temperature_sensor ambiant]
sensor_type: ATC Semitec 104GT-2
sensor_pin: P0.25
gcode_id:A

[fan]
pin: P2.3
# Load Multible Fans
#[include klipper/config/multiple_fans.cfg]

[printer]
kinematics: corexy
# This option must be "corexy" for corexy printers.
max_velocity: 250
max_accel: 1500
#max_z_velocity: 20
#max_z_accel: 25
max_z_velocity: 10
max_z_accel: 55

# "RepRapDiscount 128x64 Full Graphic Smart Controller" type displays
[display]
lcd_type: st7920
cs_pin: P1.19
sclk_pin: P1.20
sid_pin: P1.18
encoder_pins: ^P3.26, ^P3.25
click_pin: ^!P0.28
[output_pin beeper]
pin: P1.30

#kill_pin: ^!ar41

# Pause/Resume functionality with support of position capture and restore
[pause_resume]
recover_velocity: 50
#recover_velocity: 200
# When capture/restore is enabled, the speed at which to return to
# the captured position (in mm/s). Default is 50.0 mm/s.
# paste "unknownCommandsNeedAck: true" in ~/.octoprint/config.yaml
######################################
# #
# serial: #
# additionalPorts: #
# - /tmp/printer #
# baudrate: 250000 #
# disconnectOnErrors: false #
# logPositionOnCancel: true #
# port: /tmp/printer #
# unknownCommandsNeedAck: true #
# #
######################################
# Filament Switch Sensor. Support for filament insert and runout detection
# using a switch sensor, such as an endstop switch.
[filament_switch_sensor filament_sensor]
pause_on_runout: True
# When set to True, a PAUSE will execute immediately after a runout
# is detected. Note that if pause_on_runout is False and the
# runout_gcode is omitted then runout detection is disabled. Default
# is True.
runout_gcode: outoffilament
# The gcode to run after a filament runout is detected. If
# pause_on_runout is set to True this gcode will run after the PAUSE
# is complete. The default is not to run any gcode commands.
#insert_gcode:
# The gcode to run after a filament insert is detected. The default
# is not to run any gcode commands, which disables insert detection.
event_delay: 3.0
# The minimum amount of time in seconds to delay between events.
# Events triggered during this time period will be silently
# ignored. The default is 3 seconds.
switch_pin: ^z:ar15 #RAMPS Servo Pin 4
# The pin on which the switch is connected. This parameter must be
# provided.
# Idle timeout. An idle timeout is automatically enabled - add an
# explicit idle_timeout config section to change the default settings.
[idle_timeout]
#gcode:
# A list of G-Code commands (one per line; subsequent lines
# indented) to execute on an idle timeout. The default is to run
# "TURN_OFF_HEATERS" and "M84".
#timeout: 600
timeout: 1200
# Idle time (in seconds) to wait before running the above G-Code
# commands. The default is 600 seconds
#_____________________MACROS______________________________________#

#_____________________MACROS______________________________________#
[gcode_macro outoffilament]
gcode:
PARK_MACRO
;UNLOAD
M117 OUT OF FILAMENT..
[gcode_macro PARK_MACRO]
default_parameter_X: -15
default_parameter_Y: 0
default_parameter_Z: 30
gcode:
M117 PARKING..
G91
G1 E-3.14 F1500
G1 Z{Z}
G90
G1 X{X} Y{Y} F3000
[gcode_macro UNLOAD]
gcode:
G91
G1 E5.0 F1200
G1 E3.0 F1600
G1 E-25 F7000
G1 E-800 F3000
G90

[gcode_macro RESUME_MACRO]
gcode:
M117 RESUMING...
RESUME
####

#[gcode_macro M84]
#gcode:
# M18
# SET_KINEMATIC_POSITION

# Enable the "M118" and "RESPOND" extended commands.
[respond]
default_type: echo
# Sets the default prefix of the "M118" and "RESPOND" output to one of
# the following:
# echo: "echo: " (This is the default)
# command: "// "
# error: "!! "
# default_prefix: echo:
# Directly sets the default prefix. If present, this value will override
# the "default_type".

[gcode_macro G29]
gcode:
 G28
 quad_gantry_level
 BED_MESH_CALIBRATE
 BED_MESH_PROFILE SAVE=p1
 G1 X0 Y0 Z5 F3600

[quad_gantry_level]
gantry_corners:
-90,-22.5
590,495
points:
20,40
20,440
450,440
450,40
speed: 50
horizontal_move_z: 10
max_adjust: 12
#samples: 3
#sample_retract_dist: 2.0

#[quad_gantry_level]
#gantry_corners:
# 0,0
# 300,300
##	-88,-20
#	490,386
# A newline separated list of X,Y coordinates describing the
# two opposing corners of the gantry. The first entry corresponds to
# Z, the second to Z2.
# This parameter must be provided.
#points:
#	10,63
#	10,326
#	290,326
#	290,63
# A newline separated list of four X,Y points that should be probed
# during a QUAD_GANTRY_LEVEL command.
# Order of the locations is important, and should correspond to Z,Z1
# Z2, and Z3 location in order.
# This parameter must be provided.
# For maximum accuracy, ensure your probe offsets are configured.
#speed: 50
###speed: 150
# The speed (in mm/s) of non-probing moves during the calibration.
# The default is 50.
#horizontal_move_z: 10
# The height (in mm) that the head should be commanded to move to
# just prior to starting a probe operation. The default is 5
#samples: 3
# Number of probe samples per point. The defaut is 1
#sample_retract_dist: 6.0
# Distance in mm to retract the probe between samples. Default is 2.

# Mesh Bed Leveling. One may define a [bed_mesh] config section
# to enable move transformations that offset the z axis based
# on a mesh generated from probed points. Note that bed_mesh
# and bed_tilt are incompatible, both cannot be defined. When
# using a probe to home the z-axis, it is recommended to define
# a [homing_override] section in printer.cfg to home toward the
# center of the print area.
#
# Visual Examples:
# bed_shape = rectangular, probe_count = 3,3:
# x---x---x (max_point)
# |
# x---x---x
# |
# (min_point) x---x---x
#
# bed_shape = round, probe_count = 5, radius = r:
# x (0,r) end
# /
# x---x---x
# \
# (-r,0) x---x---x---x---x (r,0)
# \
# x---x---x
# /
# x (0,-r) start
#
[bed_mesh]
speed: 200
# The speed (in mm/s) of non-probing moves during the
# calibration. The default is 50.
horizontal_move_z: 10
# The height (in mm) that the head should be commanded to move to
# just prior to starting a probe operation. The default is 5.
#samples: 2
# The number of times to probe each point. The probed z-values
# will be averaged. The default is to probe 1 time.
#sample_retract_dist: 10.0
# The distance (in mm) to retract between each sample if
# sampling more than once. Default is 2mm.
mesh_min: 45,25
# Defines the minimum x,y position to probe when the bed_shape
# is 'rectangular'. Note that this refers to the nozzle position,
# take care that you do not define a point that will move the
# probe off of the bed. This parameter must be provided.
mesh_max:445,440
# Defines the maximum x,y position to probe when the bed_shape
# is 'rectangular'. Follow the same precautions as listed in min_point.
# Also note that this does not necessarily define the last point
# probed, only the maximum coordinate. This parameter must be provided.
probe_count: 4,4
## OR ##
##probe_count: 5
# For 'rectangular' beds, this is a comma separate pair of integer
# values (X,Y) defining the number of points to probe along each axis.
# A single value is also valid, in which case that value will be applied
# to both axes. 'Round' beds only accept a single integer value that is
# applied to both axes. The probe count must be odd for round beds.
# Default is 3,3 for 'rectangular' beds, and 5 for 'round' beds.
fade_start: 1
# The gcode z position in which to start phasing out z-adjustment
# when fade is enabled. Default is 1.0.
#fade_end: 10.0
fade_end: 0.0
# The gcode z position in which phasing out completes. When set
# to a value below fade_start, fade is disabled. It should be
# noted that fade may add unwanted scaling along the z-axis of a
# print. If a user wishes to enable fade, a value of 10.0 is
# recommended. Default is 0.0, which disables fade.
#
# disabling fade as per https://github.com/KevinOConnor/klipper/issues/1234
fade_target: 0
# The z position in which fade should converge. When this value is set
# to a non-zero value it must be within the range of z-values in the mesh.
# Users that wish to converge to the z homing position should set this to 0.
# Default is the average z value of the mesh.
split_delta_z: .025
# The amount of Z difference (in mm) along a move that will
# trigger a split. Default is .025.
move_check_distance: 5.0
# The distance (in mm) along a move to check for split_delta_z.
# This is also the minimum length that a move can be split. Default
# is 5.0.
#mesh_pps: 2,2
# A comma separated pair of integers (X,Y) defining the number of
# points per segment to interpolate in the mesh along each axis. A
# "segment" can be defined as the space between each probed
# point. The user may enter a single value which will be applied
# to both axes. Default is 2,2.
algorithm: bicubic
#algorithm: lagrange
# The interpolation algorithm to use. May be either "lagrange"
# or "bicubic". This option will not affect 3x3 grids, which
# are forced to use lagrange sampling. Default is lagrange.
bicubic_tension: .2
# When using the bicubic algorithm the tension parameter above
# may be applied to change the amount of slope interpolated.
# Larger numbers will increase the amount of slope, which
# results in more curvature in the mesh. Default is .2.

#*# <---------------------- SAVE_CONFIG ---------------------->
#*# DO NOT EDIT THIS BLOCK OR BELOW. The contents are auto-generated.
#*#
#*# [extruder]
#*# control = pid
#*# pid_kp = 21.512
#*# pid_ki = 1.304
#*# pid_kd = 88.737
#*#
#*# [heater_bed]
#*# control = pid
#*# pid_kp = 67.840
#*# pid_ki = 2.432
#*# pid_kd = 473.183
#*#
#*# [bed_mesh default]
#*# version = 1
#*# points =
#*#	0.292233, 0.530983, 0.431608, 0.330983
#*#	0.245358, 0.544733, 0.115358, -0.540267
#*#	-0.080892, 0.474733, -0.063392, -1.140892
#*#	-0.745267, 0.477233, 0.227233, -1.215892
#*# tension = 0.2
#*# min_x = 45.0
#*# algo = bicubic
#*# y_count = 4
#*# mesh_y_pps = 2
#*# min_y = 25.0
#*# x_count = 4
#*# max_y = 439.99
#*# mesh_x_pps = 2
#*# max_x = 444.99
#*#
#*# [bed_mesh p1]
#*# version = 1
#*# points =
#*#	0.292233, 0.530983, 0.431608, 0.330983
#*#	0.245358, 0.544733, 0.115358, -0.540267
#*#	-0.080892, 0.474733, -0.063392, -1.140892
#*#	-0.745267, 0.477233, 0.227233, -1.215892
#*# tension = 0.2
#*# min_x = 45.0
#*# algo = bicubic
#*# y_count = 4
#*# mesh_y_pps = 2
#*# min_y = 25.0
#*# x_count = 4
#*# max_y = 439.99
#*# mesh_x_pps = 2
#*# max_x = 444.99